## Slide 1: Multiple Design Representations

## Slide 2: Multiple Design Representations

## Slide 3: Multiple Design Representations

## Slide 4: Multiple Design Representations

## Slide 5: Multiple Design Representations
There are many different ways to represent design
An unlimited number!
Each depending on the performative question through which we are assessing the design
And yet there is only one design (i.e. one physical building is to be built)
So we require a degree of compatibility between these numerous representations

## Slide 6: Concepts
Object – has simple list of defining properties
- instances uniquely identifiable (Guid)
- State uniquely identifiable (Hash)
- Customisable and extendable through Fragments and Custom Data
Fragments – Objects that can be used as optional properties attached to other objects
- Can be self defining (e.g. Material)
- Can be Relational or dependant on other objects or context (e.g AdapterID)
Properties – Are classified as either:
+ Defining (e.g. BH.oM.Physical.Wall.Surface or Thickness
+ Derived (e.g. BH.oM.Physical.Wall.SurfaceArea
+ Dependant (e.g. BH.oM.Physical.Wall.AdjacentSpace)
Element – An object with some form of dimensionality
- See the IElement interfaces in Dimensional_oM

## Slide 7: Concepts
Results – xxx
Resultsets – Special cases of above Dataset where objects stored are IResults
and Source refers to a IModel instance
Dataset currently stores a list of IBHoMObject
Datasets – Curated Objects
with a Source

## Slide 8: Concepts
Specification – Written against objects defining allowable values for Properties
- These properties can be Defining, Derived or Dependant
Model – A set of compatible Objects and Specifications
- With the means to evaluate the Properties encoded in the Specification
- Requirement for Engine methods or Analysis to be available etc.
excepting of the trivial example of specification against defining properties.
- Zones
- Spatial Specification
Spatial Diffing by location…
Representational Diffing (i.e. is the Structure.Panel a compatible representation of the Physical.Floor
ToleranceSpecification coupled against Diffing.Delta (i.e. allowable variance)

## Slide 9: Concepts
Stream – A collection of objects (or Model) that is versioned and changes over time - Recording and referencing its previous states
Environment – Asynchronous Model/Task manager
Workflow – Connected associative, Synchronous chain for operations

## Slide 10: Concepts
Option

## Slide 11: Common object Model (oM)

## Slide 12: Common object Model (oM)
…
Discrete and discipline specific
+
Compatible and customisable

## Slide 13: Common object Model (oM) How to represent a “Wall”
Physical BH.oM.Physical.Elements.Wall
Analytical BH.oM.Facade.Elements.Panel
BH.oM.Structure.Elements.Panel
BH.oM.Environment.Elements.Panel
BH.oM.Acoustic.Elements.Panel
Geometrical BH.oM.Geometry.PlanarSurface
BH.oM.Geometry.NurbsSurface
BH.oM.Geometry.NurbsCurve
Graphical BH.oM.Graphics.RenderMesh

## Slide 14: Common object Model (oM)
…
…
Analytical Physical Representations
Code Framework
Dimensional Concepts
Physical Representations
Analytical Concepts
Abstract Representations
Raw Data
Base Object

## Slide 15: Key Interfaces
…
…
Elements, Materials, Results
IGeometry, ICurve, ISurface …
IResult
IBHoMObject
IElement0D, 1D, 2D …
INode, ILink, IPanel …

## Slide 16: Base BHoM Object
namespace BH.oM.Base
{
public class BHoMObject : IBHoMObject
{
/***************************************************/
/**** Properties ****/
/***************************************************/
public virtual Guid BHoM_Guid { get; set; } = Guid.NewGuid();
public virtual string Name { get; set; } = "";
public virtual FragmentSet Fragments { get; set; } = new FragmentSet();
public virtual HashSet<string> Tags { get; set; } = new HashSet<string>();
public virtual Dictionary<string, object> CustomData { get; set; } = new Dictionary<string, object>();
}
}
https://github.com/BHoM/BHoM/blob/main/BHoM/BHoMObject.cs

## Slide 17: Base BHoM Object
namespace BH.oM.Base
{
public class BHoMObject : IBHoMObject
{
/***************************************************/
/**** Properties ****/
/***************************************************/
public virtual Guid BHoM_Guid { get; set; } = Guid.NewGuid();
public virtual string Name { get; set; } = "";
public virtual FragmentSet Fragments { get; set; } = new FragmentSet();
public virtual HashSet<string> Tags { get; set; } = new HashSet<string>();
public virtual Dictionary<string, object> CustomData { get; set; } = new Dictionary<string, object>();
}
}
https://github.com/BHoM/BHoM/blob/main/BHoM/BHoMObject.cs

## Slide 18: Base BHoM Object
https://bhom.xyz/api/object.html#!?namespace=BH.oM.Base&object=BHoMObject

## Slide 19: Base BHoM Object
https://bhom.xyz/api/object.html#!?namespace=BH.oM.Base&object=BHoMObject

## Slide 20: Example: Geometry.Circle
namespace BH.oM.Geometry
{
[Description("A plane curve. Standard circle defining a curve of
constant distance from a point, its Centre.")]
public class Circle : ICurve
{
/***************************************************/
/**** Properties ****/
/***************************************************/
[Description("Origin point defining location of the Circle in three-dimensional space.")]
public virtual Point Centre { get; set; } = new Point();
[Description("Vector perpendicular to the plane in which the Circle lies.")]
public virtual Vector Normal { get; set; } = new Vector { X = 0, Y = 0, Z = 1 };
[Length]
[Description("Distance from the Centre to any point on Circle.")]
public virtual double Radius { get; set; } = 0;
https://github.com/BHoM/BHoM/blob/main/Geometry_oM/Curve/Circle.cs

## Slide 21: Example: Geometry.Circle
namespace BH.oM.Geometry
{
[Description("A plane curve. Standard circle defining a curve of
constant distance from a point, its Centre.")]
public class Circle : ICurve
{
/***************************************************/
/**** Properties ****/
/***************************************************/
[Description("Origin point defining location of the Circle in three-dimensional space.")]
public virtual Point Centre { get; set; } = new Point();
[Description("Vector perpendicular to the plane in which the Circle lies.")]
public virtual Vector Normal { get; set; } = new Vector { X = 0, Y = 0, Z = 1 };
[Length]
[Description("Distance from the Centre to any point on Circle.")]
public virtual double Radius { get; set; } = 0;
https://github.com/BHoM/BHoM/blob/main/Geometry_oM/Curve/Circle.cs
Simply, the name of the object (e.g. Circle)
and its Defining properties (e.g. Centre, Normal, Radius)
Derived properties
(e.g. Area) are all in the Engines

## Slide 22: Example: Geometry.Circle
namespace BH.oM.Geometry
{
[Description("A plane curve. Standard circle defining a curve of
constant distance from a point, its Centre.")]
public class Circle : ICurve
{
/***************************************************/
/**** Properties ****/
/***************************************************/
[Description("Origin point defining location of the Circle in three-dimensional space.")]
public virtual Point Centre { get; set; } = new Point();
[Description("Vector perpendicular to the plane in which the Circle lies.")]
public virtual Vector Normal { get; set; } = new Vector { X = 0, Y = 0, Z = 1 };
[Length]
[Description("Distance from the Centre to any point on Circle.")]
public virtual double Radius { get; set; } = 0;
https://github.com/BHoM/BHoM/blob/main/Geometry_oM/Curve/Circle.cs
Simply, the name of the object (e.g. Circle)
and its Defining properties (e.g. Centre, Normal, Radius)
Derived properties
(e.g. Area) are all in the Engines

## Slide 23: Example: Geometry.Circle
{
"_t":"BH.oM.Geometry.Circle",
"Centre":{
"_t":"BH.oM.Geometry.Point",
"X":0.0,
"Y":0.0,
"Z":0.0
},
"Normal":{
"_t":"BH.oM.Geometry.Vector",
"X":0.0,
"Y":0.0,
"Z":1.0
},
"Radius":1.0,
"_bhomVersion":"4.3"
}
https://github.com/BHoM/BHoM/blob/main/Geometry_oM/Curve/Circle.cs
Simply, the name of the object (e.g. Circle)
and its Defining properties (e.g. Centre, Normal, Radius)
Derived properties
(e.g. Area) are all in the Engines

## Slide 24: Example: Geometry.Circle Derived Properties
namespace BH.Engine.Geometry
{
public static partial class Query
{
[Description("Calculates the area of the provided geometry.")]
[Input("curve", "The Circle to get the area of.")]
[Input("tolerance", "The tolerance to apply to the area calculation.")]
[Output("area", "The area of the geometry.")]
public static double Area(this Circle curve, double tolerance = Tolerance.Distance)
{
if (curve == null)
{
BH.Engine.Reflection.Compute.RecordError("Cannot query area as the geometry is null.");
return double.NaN;
}
return Math.PI * curve.Radius * curve.Radius;
}

## Slide 25: BHoM Engine Classes
BHoM_Engine methods included in static classes relying on extension methods
There are 5 different static classes:
    Create: instantiate new objects
    Modify: modify existing objects
    Query: get derived properties from existing objects
    Convert: transform an existing object into a different type
    Compute: perform calculation given an existing object and/or some parameters
    External: reflects methods from external libraries

## Slide 26: BHoM Engine Classes Example: Geometry.Circle
BH.Engine.Geometry.Create.Circle(Point pt1, Point pt2, Point pt3, double tolerance = Tolerance.Distance)
BH.Engine.Geometry.Modify.Mirror(this Circle circle, Plane p)
BH.Engine.Geometry.Query.ClosestPoint(this Circle circle, Point point, double tolerance = Tolerance.Distance)
BH.Engine.Geometry.Convert.ToNurbsCurve(this Circle circle)
BH.Engine.Geometry.Compute.SortAlongCurve(this List<Point> points, Circle circle, double distanceTolerance = Tolerance.Distance, double angleTolerance = Tolerance.Angle)

## Slide 27: Example: Structure.Elements.Bar
https://github.com/BHoM/BHoM/blob/main/Structure_oM/Elements/Bar.cs

## Slide 28: Key Interfaces
…
…
Elements, Materials, Results
IGeometry, ICurve, ISurface …
IResult
IBHoMObject
IElement0D, 1D, 2D …
INode, ILink, IPanel …

## Slide 29: Dimensional_oM IElement Interfaces
https://github.com/BHoM/documentation/wiki/IElement-required-extension-methods

## Slide 30: Dimensional_oM IElement Interfaces
https://github.com/BHoM/documentation/wiki/IElement-required-extension-methods

## Slide 31: Analytical_oM IElement Interfaces
https://github.com/BHoM/documentation/wiki/IElement-required-extension-methods

## Slide 32: Dimensional Interfaces
https://github.com/BHoM/documentation/wiki/IElement-required-extension-methods

## Slide 33: Dimensional Interfaces
https://github.com/BHoM/documentation/wiki/IElement-required-extension-methods

## Slide 34: Dimensional Interfaces
https://github.com/BHoM/documentation/wiki/IElement-required-extension-methods

## Slide 35: Dimensional Interfaces
https://github.com/BHoM/documentation/wiki/IElement-required-extension-methods

## Slide 36: Dimensional Interfaces
https://github.com/BHoM/documentation/wiki/IElement-required-extension-methods

## Slide 37: Why all the interfaces on Elements?
Three reasons:
  A. Standardising engine methods for performing universal calculations
  B. Standardising means for consuming, visualisation and reporting elements
  C. Relate multiple representations together, convert and derive relative representations. casting relationships across transdisciplinary elements

## Slide 38: Key Interfaces
…
…
Elements, Materials, Results
IGeometry, ICurve, ISurface …
IResult
IBHoMObject
IElement0D, 1D, 2D …
INode, ILink, IPanel …

## Slide 39: Quantities_oM
[Description("Dimensional quantity as defined by the International System of Quantities")]
public abstract class QuantityAttribute : InputClassificationAttribute, IImmutable
{
[Description("Length dimension")]
public virtual int L { get; } = 0;
[Description("Mass dimension")]
public virtual int M { get; } = 0;
[Description("Time dimension")]
public virtual int T { get; } = 0;
[Description("Electric current dimension")]
public virtual int I { get; } = 0;
[Description("Temperature dimension")]
public virtual int Θ { get; } = 0;
[Description("Amount of substance dimension")]
public virtual int N { get; } = 0;
[Description("Luminous intensity dimension")]
public virtual int J { get; } = 0;
[Description("SI derived unit symbol")]
public abstract string SIUnit { get; }
}

## Slide 40: Quantities_oM
[AttributeUsage(AttributeTargets.Property)]
public class Density : QuantityAttribute
{
/***************************************************/
/**** Properties ****/
/***************************************************/
public override int M { get; } = 1;
public override int L { get; } = -3;
public override string SIUnit { get; } = "kg/m³";
/***************************************************/
}

## Slide 41: Quantities_oM
[Description("Structural steel material to be used on structural elements and properties or as a fragment of the physical material.")]
public class Steel : BHoMObject, IIsotropic
{
/***************************************************/
/**** Properties ****/
/***************************************************/
[Description("A unique Name is required for some structural packages to create and identify the object.")]
public override string Name { get; set; }
[Density]
public virtual double Density { get; set; }
[Ratio]
[Description("Dynamic damping ratio, expressed as a ratio between actual damping and critical damping. For structures, typically taken as 0.02 (i.e. 2%).")]
public virtual double DampingRatio { get; set; }
[Ratio]
[Description("Ratio between axial and transverse strain. Used together with YoungsModulus to derive the ShearModulus for isotropic materials.")]
public virtual double PoissonsRatio { get; set; }
[ThermalExpansionCoefficient]
[Description("The strain induced in the material per unit change of temperature.")]
public virtual double ThermalExpansionCoeff { get; set; }
[YoungsModulus]
[Description("Modulus of elasticity of the material. Ratio between axial stress and axial strain.")]
public virtual double YoungsModulus { get; set; }
[Stress]
[Description("The stress required for the material to yield.")]
public virtual double YieldStress { get; set; }
[Stress]
[Description("The stress required for the material to fail.")]
public virtual double UltimateStress { get; set; }

## Slide 42: Quantities_oM

## Slide 43: Key Interfaces
…
…
Elements, Materials, Results
IGeometry, ICurve, ISurface …
IResult
IBHoMObject
IElement0D, 1D, 2D …
INode, ILink, IPanel …

## Slide 44: BH.oM.Geometry

## Slide 45: BH.oM.Geometry 0D

## Slide 46: BH.oM.Geometry 1D

## Slide 47: BH.oM.Geometry 2D

## Slide 48: BH.oM.Geometry 3D

## Slide 49: BH.oM.Geometry Mesh

## Slide 50: Results and the IImmutable interface
https://github.com/BHoM/documentation/wiki/The-IImmutable-interface
[Description("Base class for all bar result classes. Stores all identifier information and
how to sort the results in a collection.")]
public abstract class BarResult : IStructuralResult, IImmutable

## Slide 51: Results and the IImmutable interface
https://github.com/BHoM/documentation/wiki/The-IImmutable-interface
[Description("Resulting section forces in local coordinates along the bar.")]
public class BarForce : BarResult
{
/***************************************************/
/**** Properties ****/
/***************************************************/
[Force]
[Description("Axial force along the local x-axis. Positive for tension, negative for compression.")]
public virtual double FX { get; }
[Force]
[Description("Shear force along the local y-axis. Generally minor axis shear force.")]
public virtual double FY { get; }
[Force]
[Description("Shear force along the local z-axis. Generally major axis shear force.")]
public virtual double FZ { get; }
[Moment]
[Description("Torsional moment.")]
public virtual double MX { get; }
[Moment]
[Description("Bending moment about the local y-axis. Generally major axis bending moment.")]
public virtual double MY { get; }
[Moment]
[Description("Bending moment about the local z-axis. Generally minor axis bending moment.")]
public virtual double MZ { get; }

## Slide 52: Key Interfaces
…
…
Elements, Materials, Results
IGeometry, ICurve, ISurface …
IResult
IBHoMObject
IElement0D, 1D, 2D …
INode, ILink, IPanel …

## Slide 53: Common object Model (oM)
Total number of objects is currently 1467
Organised across 26 wide ranging disciplines/namespaces:
Acoustic
Analytical
Architecture
Data
Deep Learning
Diffing
Dimensional
Environment
Façade
Geometry
Graphics
Humans
Inspections
Life Cycle Assessment
Lighting
MEP
Physical
Planning
Programming
Quantities
Reflection
Security
Spatial
Structure
Test
Versioning

## Slide 54: Elements
IElement1D
BH.oM.MEP.System.WireSegment
BH.oM.MEP.System.Pipe
BH.oM.MEP.System.FlowSystem
BH.oM.MEP.System.Duct
BH.oM.MEP.System.CableTray
BH.oM.Adapters.GSA.Elements.Spacer
BH.oM.Facade.Elements.FrameEdge
BH.oM.Structure.Elements.Edge
BH.oM.Structure.Elements.Bar
BH.oM.MEP.Fixtures.Sprinkler
BH.oM.Environment.Elements.Edge
BH.oM.Physical.Elements.Pile
BH.oM.Physical.Elements.Column
BH.oM.Physical.Elements.Cable
BH.oM.Physical.Elements.Bracing
BH.oM.Physical.Elements.Beam
BH.oM.Spatial.SettingOut.Grid
BH.oM.Geometry.Polyline
BH.oM.Geometry.PolyCurve
BH.oM.Geometry.NurbsCurve
BH.oM.Geometry.Line
BH.oM.Geometry.Ellipse
BH.oM.Geometry.Circle
BH.oM.Geometry.Arc
IElement2D
BH.oM.Facade.Elements.Panel
BH.oM.Facade.Elements.Opening
BH.oM.Facade.Elements.CurtainWall
BH.oM.Structure.Elements.Panel
BH.oM.Structure.Elements.Opening
BH.oM.Structure.Reinforcement.ReinforcementRegion
BH.oM.Environment.Elements.Zone
BH.oM.Environment.Elements.Space
BH.oM.Environment.Elements.Panel
BH.oM.Environment.Elements.Opening
BH.oM.Physical.Elements.Window
BH.oM.Physical.Elements.Wall
BH.oM.Physical.Elements.Void
BH.oM.Physical.Elements.Roof
BH.oM.Physical.Elements.Floor
BH.oM.Physical.Elements.Door
BH.oM.Architecture.Elements.Room
BH.oM.Architecture.Elements.CeilingTile
BH.oM.Architecture.Elements.Ceiling
BH.oM.Geometry.PlanarSurface
IElement0D
BH.oM.Security.Elements.CameraDevice
BH.oM.MEP.Equipment.MechanicalEquipment
BH.oM.MEP.Equipment.ElectricalEquipment
BH.oM.MEP.Fixtures.PlumbingFixture
BH.oM.MEP.Fixtures.LightFixture
BH.oM.MEP.Fixtures.FireAlarmDevice
BH.oM.MEP.Fixtures.ElectricalFixture
BH.oM.MEP.Fixtures.AirTerminal
BH.oM.MEP.System.Dampers.Valve
BH.oM.MEP.System.Dampers.VolumeDamper
BH.oM.MEP.System.Dampers.Damper
BH.oM.MEP.System.Fittings.Fitting
BH.oM.MEP.System.Node
BH.oM.Lighting.Analysis.Node
BH.oM.Lighting.Elements.Luminaire
BH.oM.Structure.Elements.Node
BH.oM.Environment.Analysis.Node
BH.oM.Architecture.BuildersWork.Opening
BH.oM.Graphics.RenderPoint
BH.oM.Geometry.Point

## Slide 55: Objects are not useful in isolation

## Slide 56: BHoM Adapter Toolkits Interoperability with common oM
36 Open Source Adapters
currently (and growing)

## Slide 57: BHoM Adapter Toolkits Interoperability with common oM
Structure
Environment
Geometry
Physical
Spatial
…
…
…
…
Structure.Elements
Loads
Analysis Results
Material Properties

## Slide 58: Why all the interfaces on Elements?
Three reasons:
  A. Standardising engine methods for performing universal calculations
  B. Standardising means for consuming, visualisation and reporting elements
  C. Relate multiple representations together, convert and derive relative representations. casting relationships across transdisciplinary elements

## Slide 59
  A. Standardising engine methods for performing universal calculations
Spatial Engine – Model Laundry
Graph and topology queries - Graphflow
Matter Engine
Life Cycle Assessment
Data processing and analytics

## Slide 60
IElements
Dimensional
Quantities
Base Object
Geometry
Analytical
IResults
Graphics
Game Engines
+
3D Viewers
+
Dashboards
  B. Standardising means for consuming, visualisation and reporting elements
IGeometry

## Slide 61
  C. Relate multiple representations together, convert and derive relative representations. casting relationships across transdisciplinary elements
IElements
IModel
ISystem
Transdisciplinary
Scripts

## Slide 62: How to link single (semi-autonomous) models together
What are we doing now?
What new concepts we need to formalise:
  ISpecification (extension of CIH work)
  IModel and IControlSystem
  IStream (integration with Deltas work)
What is the difference between Physical/Analytical Explicit? Geometrical?
Design coordination happens in Physical/Explict? These are the components used to define Components

## Slide 63: What are we doing now?

## Slide 64: IElement & IResults control systems

## Slide 65: IElement & IResults control systems IModel

## Slide 66: IElement & IResults control systems Iterative/autonomous IModel

## Slide 67: IElement & IResults control systems Iterative/autonomous, with reporting

## Slide 68: IElement & IResults control systems Iterative/autonomous, with reporting, human control

## Slide 69: IElement & IResults control systems Iterative/autonomous with reporting + human control

## Slide 70: IElement & IResults control systems Iterative/autonomous with reporting + human control

## Slide 71: 1. Chaining Distributed UIs but with potential for common overlaid central Design Environment
Common Design Environment
one way - output

## Slide 72: 2. Wrapping Centralised UI and Presentation layer driving processes
Common Design Environment

## Slide 73: 3. Integration Common hosting and processing environment
Common Design Environment

## Slide 74: Multiple Design Representations

## Slide 75: Rapid Prototyping
Calibration > Building > Experience
Reference 2
Future
Reference 1
Specific Project
Reference Criterion 1
Reference Criterion 2
Analysis and Calibration
Analysis and Interpretation of Reference Parameters
Mapping of Reference Parameters
Specific Project Work (in planning)
Calibration (in existence)
Past
Link Weightings
Link Weightings
PERFORMANCE CRITERIA
DESIGN PARAMETERS
BUILDING ELEMENTS
Performance Criterion
Notes: No master layout—copy/paste directly from this slide.

## Slide 76
Composite Parameter
--------
--------
--------
--------
CP0
Comparison
Augment Base Parameters
To achieve
Target CP*
CP1..n
Render
Design Options
Base Parameters
Render
Base Condition
Render
Compliance
Directly Augment Base Parameters
To achieve
Compliance

## Slide 77
Composite Parameter A
--------
--------
--------
CP0
Comparison
Augment Base Parameters
To achieve
Target CP*
CP1..n
Render
Design Options
Base Parameters
Render
Base Condition
Render
Compliance
Directly Augment Base Parameters
To achieve
Compliance
Parameters
Parameters
SITE
Ref.
ENVIRONMENT
1
Ref.
ENVIRONMENT
2
…
CP1
CP2
Composite Parameter A
Composite Parameter A
weightings
Calibration
Consultation

## Slide 78: Coordinated Computational Development Map
database architecture and access
code hosting and deployment
code framework
datasets and model libraries
adapters
engines
data analytics
visualisations
scripts + workflows
code
hosting
engines
analytics
adapters
adapters
datasets
databases
oM
oM
oM
visual reporting
tools
game engines
web platform
3D + data visualisation
single coordinated platform

## Slide 79
Object Instances
Object Specifications
Common Object Schema
Common Repositories
Users
Configurators

## Slide 80: Digital Configurator| Executive Summary
A Configurator as part of a Common Configurator Framework
Object Instances Repo
Configurator
Common Object
Schema
Specification Repo
Object Instances Repo
Specification Repo
User

## Slide 81: Digital Configurator| Executive Summary
A Configurator as part of a Common Configurator Framework

## Slide 84
Composite Parameter
--------
--------
--------
--------
CP0
Comparison
Augment Base Parameters
To achieve
Target CP*
CP1..n
Render
Design Options
Base Parameters
Render
Base Condition
Render
Compliance
Directly Augment Base Parameters
To achieve
Compliance

## Slide 85
Composite Parameter A
--------
--------
--------
CP0
Comparison
Augment Base Parameters
To achieve
Target CP*
CP1..n
Render
Design Options
Base Parameters
Render
Base Condition
Render
Compliance
Directly Augment Base Parameters
To achieve
Compliance
Parameters
Parameters
SITE
Ref.
ENVIRONMENT
1
Ref.
ENVIRONMENT
2
…
CP1
CP2
Composite Parameter A
Composite Parameter A
weightings
Calibration
Consultation

## Slide 86: Use Rebar 4.0 as example
How do these representations all relate? Cross reference each other?
Floor
Rebar Intent
Rebar
3D Rebar
3D Rebar
Revit
Structure
Structure
Fabrication
Site Survey
3D Rebar
Physical
Slab
Physical
Revit
Rebar
IFC
Rebar
ETABS
Slab
Panel
Structure
Results
Structure
IFC
Slab
Ledger GUIDS
ETABS
Results
Rebar
3DRepo
Cares Cloud

## Slide 88
IFC Beam | BH.oM.Physical.Beam | BHoM.Structure.Bar | Etabs Bar | Rebartek | Site
idfjreerwr | reerw | 32434 | 45 | 54454 | 8889
Element

## Slide 89: Notes
USD
Bar – Analytical - ILink
FramingElement – Geometrical – ICurve
    Both are IElement1D
Explit (